## Slide 1
陳培殷
國立成功大學 資訊工程系
數位系統實驗
Thu 9:00 pm – 12:00 pm

## Slide 2
陳培殷
國立成功大學 資訊工程系
LAB - 02

## Slide 3: Outline (9/30)
Boolean Algebra Part 1 (影片 13:34)
Boolean Algebra Part 2 (影片 9:34)
Lab2_1 (線上)
  Lab2_1_1 (影片2:35)
  Lab2_1_2 (影片0:49)
Lab2_2 & Lab2_3 (線上)
  Lab2_2 (影片2:44)
  Lab2_3 (影片1:55)

## Slide 4: Three representations for a circuit
F1=x+y’z
1. Boolean Algebra
3. Circuit Diagram
2. Truth Table
Inputs
n input variables  2n combinations
真值表

## Slide 5: Equipment
Names | Amount
Solerless Breadboard | ×1
74LS00 | ×1
74LS04 | ×1
74LS08 | ×1
74LS32 | ×1

## Slide 6: Lab notice
Input
Output

## Slide 7: Lab 02_1
Please draw their Truth Tables and implement the circuits with breadboard.
  F1(A, B) = (A + B)’(A’ + B’)
  F2(A, B) = A’+ AB
A | B | F1
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | F2
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Notes: 錯誤：此時不需化簡(已修正)

## Slide 8: Lab notice
Correct
VCC：
GND：

## Slide 9: Lab notice
Wrong
Overlap

## Slide 10: Lab notice
Correct
VCC：
GND：

## Slide 11: Lab notice
Correct
VCC：
GND：

## Slide 12: Lab notice
A
B
A
B

## Slide 13: Lab notice
A
B
A

## Slide 14
  A half adder (HA) consists of two inputs (A and B) and two outputs (Sum and Carry). “A” denotes the summand and “B” is the addend. Sum and Carry mean the output sum and carry for input “A” and “B”. The truth table and Boolean algebra for the half adder are as follows.
A | B | Sum | Carry
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
  F(A, B) = A’B’ + A’B + AB’ + AB
Lab 02_2 - Half Adder (1/2)

## Slide 15
Please
  (a) draw the circuit diagram of the half adder according
  to the truth table shown in previous page.
  (b) implement the circuit on the breadboard.
Lab 02_2 - Half Adder (2/2)

## Slide 16
There are two inputs denoted as A and B. Both A and B are 1-bit value. A comparator is designed to determine whether A is equal to B or not. The output results are represented with E .
  E =
Lab 02_3 – Comparator(1/2)

## Slide 17
Please
  (a) draw the truth table of the comparator.
  (b) draw the circuit diagram of the comparator.
  (c) implement the circuit on the breadboard.
A | B | F
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
  F(A, B) = (A’B’) + (AB)
  F(A, B) = A’B’ + A’B + AB’ + AB
Lab 02_3 – Comparator(2/2)