## Slide 1: LAB - 04
陳培殷
國立成功大學 資訊工程系

## Slide 2: Outline
Video preview for 晶片實現+HDL介紹(Parts II~IV)
Quartus II tutorial
Introduction to DE0-CV
Programming DE0-CV
Lab I – adder-subtractor to DE0-CV
Lab II – encoder to DE0-CV

## Slide 3: Quartus II Tutorial (1/10)
Getting Started –
  Start the Quartus II software

## Slide 4
Quartus II Tutorial (2/10)
Create a New Project –
  Open New Project Wizard (File → New Project Wizard…)

## Slide 5
Specify the working directory and the name of the project
可先新增資料夾
請記住!名稱要相同
Quartus II Tutorial (3/10)

## Slide 6: Quartus II Tutorial (4/10)
Select “Empty project”. Then, click “Next”.
Select design files. Or click “Next” to skip this step.

## Slide 7: Quartus II Tutorial (5/10)
Specify device settings - (DE0-CV Device family are used). Click “Next.”
5CEFA4F23C7

## Slide 8: Quartus II Tutorial (6/10)
Specify EDA Tool – (Modelsim-Altera is selected for simulation). Click “Finish.”

## Slide 9: Quartus II Tutorial (7/10)
Edit a new file by opening a Verilog HDL file
  (File → New → Verilog HDL File → OK)

## Slide 10: Quartus II Tutorial (8/10)
Write Verilog code
Top module name 一定要跟 Project name 相同 !!
輸入(input) |  | 輸出(output) | 
被加數(a) | 加數(b) | 和(sum) | 進位(carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1: | //File Name：Half_Adder.v
2: | module Half_Adder(a, b, sum, carry);
3: | input a, b;
4: | output sum, carry;
5: | 
6: | assign sum = a ^ b;
7: | assign carry = a & b;
8: | 
9: | endmodule

## Slide 11: Quartus II Tutorial (9/10)
Compiling the Designed Circuit (synthesis 合成)
  (Processing → Start Compilation)

## Slide 12: Quartus II Tutorial (10/10)
Successful compilation

## Slide 13: Outline
Video preview for 晶片實現+HDL介紹(Parts II~IV)
Quartus II tutorial
Introduction to DE0-CV
Programming DE0-CV
Lab I – adder-subtractor to DE0-CV
Lab II – encoder to DE0-CV

## Slide 14: Introduction to DE0-CV(1/3)
DE0-CV is a FPGA simulation board used to simulate the user-defined circuit.
You can program you circuit into the FPGA in the board for simulation.
User-defined circuit

## Slide 15: Introduction to DE0-CV (2/3)
USB
電源

## Slide 16: Introduction to DE0-CV (3/3)
inputs
outputs
Traditional simulation
Solderless Breadboard
FPGA
Simulation
your circuit

## Slide 17: Outline
Video preview for 晶片實現+HDL介紹(Parts II~IV)
Quartus II tutorial
Introduction to DE0-CV
Programming DE0-CV
Lab I – adder-subtractor to DE0-CV
Lab II – encoder to DE0-CV

## Slide 18: Programming DE0-CV (1/13)

## Slide 19: Programming DE0-CV (2/13)
Start compilation

## Slide 20: Programming DE0-CV (3/13)
Open Pin Planner

## Slide 21: Programming DE0-CV (4/13)
Pin assignment
Double click

## Slide 22: Programming DE0-CV (5/13)
Assign pin location to all inputs and outputs
  Please refer to DE0_pin.xls for pin location assignment
SW0
SW1
LED1
LED0

## Slide 23: Programming DE0-CV (6/13)
Start compilation

## Slide 24: Programming DE0-CV (7/13)
右鍵選更新驅動程式軟體

## Slide 25: Programming DE0-CV (8/13)

## Slide 26: Programming DE0-CV (9/13)
Quartus Lite安裝路徑下

## Slide 27: Programming DE0-CV (10/13)

## Slide 28: Programming DE0-CV (11/13)
Programming device

## Slide 29: Programming DE0-CV (12/13)
Hardware setup: add USB-Blaster
Double click
1
2
3

## Slide 30: Programming DE0-CV (13/13)
Programming device

## Slide 31: Outline
Video preview for 晶片實現+HDL介紹(Parts II~IV)
Quartus II tutorial
Introduction to DE0-CV
Programming DE0-CV
Lab I – adder-subtractor to DE0-CV
Lab II – encoder to DE0-CV

## Slide 32: Lab I -- Adder-Subtractor to DE0-CV
請設計一 2-bit 無號數加減法器，並燒錄至DE0-CV開發板
  Input: a(2 bits)、b(2 bits)、select(1 bit)
  Output: out(2 bits)、overflow(1 bit)
無號數加減法器藉由選擇(select)訊號決定進行加法或減法運算
  select訊號為1時，out輸出a + b
  select訊號為0時，out輸出a - b
  溢位(overflow)訊號用來表示有無進位或借位

## Slide 33: Lab I -- Adder-Subtractor to DE0-CV
Hint:
  可利用三元運算子或behavior description中的if-else語法來依照select訊號完成電路
  可使用concatenation來簡化運算
  電路運作模式參考1-bit 加減法器之真值表

## Slide 34: Lab I -- Adder-Subtractor to DE0-CV
完成verilog電路設計後，需先確認其在Quartus可順利編譯，再將其燒錄至DE0-CV開發板進行驗證
使用Switch(SW0~SW4)控制input訊號，使用LED(LED0~LED2)表示output
SW0~SW1
SW2~SW3
SW4
LED0~LED1
LED2
確定編譯成功

## Slide 35: Outline
Video preview for 晶片實現+HDL介紹(Parts II~IV)
Quartus II tutorial
Introduction to DE0-CV
Programming DE0-CV
Lab I – adder-subtractor to DE0-CV
Lab II – encoder to DE0-CV

## Slide 36: Lab II -- encoder to DE0-CV
請設計一4對2編碼器(4 to 2 encoder)
編碼器可以將2n個輸入訊號轉換成n位元輸出訊號，假設有m個輸入與n個輸出，則稱為m對n編碼器
Hint: 可使用behavior description之case語法實作
輸入(input) |  |  |  | 輸出(output) |  | 
in[3] | in[2] | in[1] | in[0] | valid | out[1] | out[0]
0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1 | 1
其餘的輸入情況 |  |  |  | 0 | 0 | 0

## Slide 37: Lab II -- encoder to DE0-CV
完成verilog電路設計後，需先確認其在Quartus可順利編譯，再將其燒錄至DE0-CV開發板進行驗證
使用Switch(SW0~SW3)控制input訊號，使用LED(LED0~LED2)表示output
確定編譯成功
SW0~SW3
LED0~LED1
LED2

## Slide 38
Notice
請勿命名中文資料夾
Device family 請確認與 FPGA Chip 符合 (5CEBA4F23C7)
Top module name & Project name 需要一致

## Slide 39: Appendix
為了幫助同學驗證程式是否正確，moodle上有提供testbench
驗證方式:
  Step 1: 前往verilog線上模擬網站: https://www.jdoodle.com/execute-verilog-online/
  Step 2: 將moodle上的testbench code整段貼上
  Step 3: 修改adder_subtractor/encoder module
  Step 4: 按下Execute按鈕，確認模擬結果是否正確
Step 2 & step 3
Step 4

## Slide 40: Appendix
Lab 4-1 模擬結果

## Slide 41: Appendix
Lab 4-2 模擬結果