## Slide 1: LAB - 05
陳培殷
國立成功大學 資訊工程系

## Slide 2: Outline
Video preview for 晶片實現+HDL介紹(Parts I~V)
Seven segment display
Lab I – 學號顯示器
Lab II – 3-bit Adder
Appendix

## Slide 3: Seven-segment display (1/3)

## Slide 4: Seven-segment display (2/3)
0 is on, 1 is off
dp is useless in DE0-CV board
Ex: out=7'b1000000;
Ex: out=7'b0010010;
g=1
b=1, e=1

## Slide 5: Seven-segment display (3/3)
Assign out to seven segment digit pin of FPGA
  Take seven segment digit 0 as example
Signal Name | FPGA Pin No. | Description | Signal Assigned
HEX00 | PIN_U21 | Seven Segment Digit 0[0] | out[0]
HEX01 | PIN_V21 | Seven Segment Digit 0[1] | out[1]
HEX02 | PIN_W22 | Seven Segment Digit 0[2] | out[2]
HEX03 | PIN_W21 | Seven Segment Digit 0[3] | out[3]
HEX04 | PIN_Y22 | Seven Segment Digit 0[4] | out[4]
HEX05 | PIN_Y21 | Seven Segment Digit 0[5] | out[5]
HEX06 | PIN_AA22 | Seven Segment Digit 0[6] | out[6]

## Slide 6: Outline
Video preview for 晶片實現+HDL介紹(Parts I~V)
Seven segment display
Lab I – 學號顯示器
Lab II – 3-bit Adder
Appendix

## Slide 7: Lab I 學號顯示器
設計一個學號顯示器電路，顯示學號的後三碼
輸出21bits (使用三個七段顯示器，每個七段顯示器需用7bits控制亮暗)
Ex: 學號F12345678，七段顯示器顯示678
HEX26~HEX20, HEX16~HEX10, HEX06~HEX00

## Slide 8: Lab II – 3-bit Adder
設計一3-bit無號數加法器，輸入兩個3 bits數字，以七段顯示器顯示加法運算結果(16進制)
3 bits加法和的大小在0~15之間，使用0~9、a~f表示
Input: a(3 bits)、b(3 bits)
Output: out(7 bits)
HEX06~HEX00

## Slide 9: Notice for Lab II
七段顯示器裝置模擬
  EX: a = 0, b = 1
  七段顯示器顯示1
  EX: a = 3, b = 4
  七段顯示器顯示7
  EX: a = 7, b = 7
  七段顯示器顯示E

## Slide 10
Notice
請勿命名中文資料夾
Device family 請確認與 FPGA Chip 符合 (5CEFA4F23C7)
Top module name & Project name 需要一致

## Slide 11: Outline
Video preview for 晶片實現+HDL介紹(Parts I~V)
Seven segment display
Lab I – 學號顯示器
Lab II – 3-bit Adder
Appendix

## Slide 12: Quartus II Tutorial (1/10)
Getting Started –
  Start the Quartus II software

## Slide 13
Quartus II Tutorial (2/10)
Create a New Project –
  Open New Project Wizard (File → New Project Wizard…)

## Slide 14
Specify the working directory and the name of the project
可先新增資料夾
請記住!名稱要相同
Quartus II Tutorial (3/10)

## Slide 15: Quartus II Tutorial (4/10)
Select “Empty project”. Then, click “Next”.
Select design files. Or click “Next” to skip this step.

## Slide 16: Quartus II Tutorial (5/10)
Specify device settings - (DE0-CV Device family are used). Click “Next.”
5CEFA4F23C7

## Slide 17: Quartus II Tutorial (6/10)
Specify EDA Tool – (Modelsim-Altera is selected for simulation). Click “Finish.”

## Slide 18: Quartus II Tutorial (7/10)
Edit a new file by opening a Verilog HDL file
  (File → New → Verilog HDL File → OK)

## Slide 19: Quartus II Tutorial (8/10)
Write Verilog code
Top module name 一定要跟 Project name 相同 !!
輸入(input) |  | 輸出(output) | 
被加數(a) | 加數(b) | 和(sum) | 進位(carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1: | //File Name：Half_Adder.v
2: | module Half_Adder(a, b, sum, carry);
3: | input a, b;
4: | output sum, carry;
5: | 
6: | assign sum = a ^ b;
7: | assign carry = a & b;
8: | 
9: | endmodule

## Slide 20: Quartus II Tutorial (9/10)
Compiling the Designed Circuit (synthesis 合成)
  (Processing → Start Compilation)

## Slide 21: Quartus II Tutorial (10/10)
Successful compilation

## Slide 22: Programming DE0-CV (1/13)

## Slide 23: Programming DE0-CV (2/13)
Start compilation

## Slide 24: Programming DE0-CV (3/13)
Open Pin Planner

## Slide 25: Programming DE0-CV (4/13)
Pin assignment
Double click

## Slide 26: Programming DE0-CV (5/13)
Assign pin location to all inputs and outputs
  Please refer to DE0_pin.xls for pin location assignment
SW0
SW1
LED1
LED0

## Slide 27: Programming DE0-CV (6/13)
Start compilation

## Slide 28: Programming DE0-CV (7/13)
右鍵選更新驅動程式軟體

## Slide 29: Programming DE0-CV (8/13)

## Slide 30: Programming DE0-CV (9/13)
Quartus Lite安裝路徑下

## Slide 31: Programming DE0-CV (10/13)

## Slide 32: Programming DE0-CV (11/13)
Programming device

## Slide 33: Programming DE0-CV (12/13)
Hardware setup: add USB-Blaster
Double click
1
2
3

## Slide 34: Programming DE0-CV (13/13)
Programming device