## Slide 1
陳培殷
國立成功大學 資訊工程系
LAB - 06
Notes: 題目有點太少

## Slide 2: Outline
Video preview for 晶片實現 + HDL介紹 (Parts VI)
Sequential Circuit
Lab I – Counter (sequential circuit)

## Slide 3
Sequential Circuit (1/3)
A sequential circuit is a system whose outputs at any time are determined from the present combination of inputs and the previous inputs or outputs.
Combinational
Logic Circuit
..
..
n input
variables
m output
variables
Memory
Elements
states
Sequential components contain memory elements
The output values of sequential components depend on the input values and the values stored in the memory elements

## Slide 4
Sequential Circuit (2/3)
正緣同步電路
低位準非同步重置

## Slide 5
Sequential Circuit (3/3)
Blocking statement vs nonblocking statement

## Slide 6: Lab I (1/3)
請設計一個具備下列功能的計數器：
  正緣同步電路，低位準非同步重置
  當reset訊號為0，將目前狀態暫停，輸出維持0
  當reset訊號為1，每秒計數加1
    EX：0 -> 1 -> 2 -> …… -> E -> F -> 0 -> ……
  FPGA版之clock頻率為50MHz，需藉由除頻器將clock訊號降為1Hz
    實現方式為透過一個計數器，計算經過幾個時脈正緣，當計數到50 × 106 即代表經過一秒
Notes: 可解釋為overflow

## Slide 7: Lab I (2/3)
請將計數的數值顯示於七段顯示器
系統架構圖請參考下方
  Input ：clock(CLOCK_50) , reset(SW0)
  Output ：out(7 bits，HEX06~HEX00)
可使用structural description設計，其中，除頻器及計數模組為循序電路，七段顯示器控制模組則為組合電路

## Slide 8: Lab I (3/3)
輸出範例
reset
t = 1
t = 2
t = 3
…
t = 16

## Slide 9: Lab - Hint(1/2)
Frequency Divider (sequential circuit)
  將clock頻率從50MHz降為1Hz
Counter (sequential circuit)
  每秒進行計數
Seven Display (combinational circuit)
  將Counter數值轉為七段顯示器控制訊號
Module呼叫範例 (Structural description)
  FrequencyDivider u_FreqDiv (.clk(clock), .reset(reset), .clk_div(clock_div));
  Counter u_counter(.clk(clock_div), .reset(reset), .count(count));
  SevenDisplay u_display(.count(count), .out(out));
.port_name(signal_name)
module_name unit_name

## Slide 10: Lab – Hint(2/2)
除頻器範例：
  每0.5秒改變一次訊號(div_clk)
低位準同步reset

## Slide 11: Seven-segment display(1/2)

## Slide 12: Seven-segment display (2/2)
0 is on, 1 is off
dp is useless in DE0-CV board
Ex: out=7'b1000000;
Ex: out=7'b0010010;
g=1
b=1, e=1

## Slide 13
Notice
請勿命名中文或數字開頭的資料夾
Device family 請確認與 FPGA Chip 符合 (5CEFA4F23C7)
Top module name & Project name 需要一致

## Slide 14: Quartus II Tutorial (1/10)
Getting Started –
  Start the Quartus II software

## Slide 15
Quartus II Tutorial (2/10)
Create a New Project –
  Open New Project Wizard (File → New Project Wizard…)

## Slide 16
Specify the working directory and the name of the project
可先新增資料夾
請記住!名稱要相同
Quartus II Tutorial (3/10)

## Slide 17: Quartus II Tutorial (4/10)
Select “Empty project”. Then, click “Next”.
Select design files. Or click “Next” to skip this step.

## Slide 18: Quartus II Tutorial (5/10)
Specify device settings - (DE0-CV Device family are used). Click “Next.”
5CEFA4F23C7

## Slide 19: Quartus II Tutorial (6/10)
Specify EDA Tool – (Modelsim-Altera is selected for simulation). Click “Finish.”

## Slide 20: Quartus II Tutorial (7/10)
Edit a new file by opening a Verilog HDL file
  (File → New → Verilog HDL File → OK)

## Slide 21: Quartus II Tutorial (8/10)
Write Verilog code
Top module name 一定要跟 Project name 相同 !!
輸入(input) |  | 輸出(output) | 
被加數(a) | 加數(b) | 和(sum) | 進位(carry)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1: | //File Name：Half_Adder.v
2: | module Half_Adder(a, b, sum, carry);
3: | input a, b;
4: | output sum, carry;
5: | 
6: | assign sum = a ^ b;
7: | assign carry = a & b;
8: | 
9: | endmodule

## Slide 22: Quartus II Tutorial (9/10)
Compiling the Designed Circuit (synthesis 合成)
  (Processing → Start Compilation)

## Slide 23: Quartus II Tutorial (10/10)
Successful compilation

## Slide 24: Programming DE0-CV (1/13)

## Slide 25: Programming DE0-CV (2/13)
Start compilation

## Slide 26: Programming DE0-CV (3/13)
Open Pin Planner

## Slide 27: Programming DE0-CV (4/13)
Pin assignment
Double click

## Slide 28: Programming DE0-CV (5/13)
Assign pin location to all inputs and outputs
  Please refer to DE0_pin.xls for pin location assignment
SW0
SW1
LED1
LED0

## Slide 29: Programming DE0-CV (6/13)
Start compilation

## Slide 30: Programming DE0-CV (7/13)
右鍵選更新驅動程式軟體

## Slide 31: Programming DE0-CV (8/13)

## Slide 32: Programming DE0-CV (9/13)
Quartus Lite安裝路徑下

## Slide 33: Programming DE0-CV (10/13)

## Slide 34: Programming DE0-CV (11/13)
Programming device

## Slide 35: Programming DE0-CV (12/13)
Hardware setup: add USB-Blaster
Double click
1
2
3

## Slide 36: Programming DE0-CV (13/13)
Programming device